## Slide 1: YANG models for Systems with Link Aggregation
Scott Mansfield
Stephen Haddock
October 6, 2025

## Slide 2: Introduction
  This presentation provides a simple example of modifying the YANG model for a system without Link Aggregation to a system with Link Aggregation.
  A bridge is used as an example system, however adapting this to a system with different functionality simply involves replacing bridge-specific containers with appropriate containers for the other system functionality.
  YANG configuration files in JSON and XML are provided for the examples.

## Slide 3: Simple Example
Connect two generic boxes with a single link
Convert the connection to a Link Aggregation Group (LAG)
Box 1a
Box 2a
Box 1b
Box 2b

## Slide 4: Assume the boxes are bridges
Box 1a “baggy pants” diagram
  MAC Relay has two ports.
  Each MAC attached to a port on the relay.
Box 1b “baggy pants” diagram
  MAC Relay still has two ports.
  MAC-1 attached directly to the relay.
  MAC-2 and MAC-3 each attach to an Aggregation Port in a Link Aggregation Sublayer.
  The Link Aggregation Sublayer has a single Aggregator that attaches to the relay.
Box 1b
MAC Relay
Aggregator
Agg Port
Agg Port
Box 1a
MAC Relay
MAC-1
MAC-1
MAC-2
MAC-2
MAC-3
()
()
()
()
()
()

## Slide 5
[ bridge-port ]
[ ethernet ]
ethernetCsmacd
MAC-1
bridge
component
[ bridge-port ]
[ ethernet ]
ethernetCsmacd
MAC-2
Box 1a YANG Model
Interface of type ethernetCsmacd augmented with ethernet and bridge-port containers
bridges list containing a single bridge, in turn containing a single component
bridges
interface of type ethernetCsmacd augmented with ethernet and bridge-port containers
bridge-port container includes a leaf that points to the component to which this interface is attached

## Slide 6
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-2
[ bridge-port ]
[ ethernet ]
ethernetCsmacd
MAC-1
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-3
Still have two interfaces with bridge-port containers pointing to the bridge component
Add interface of type ieee8023adLag augmented with lag and bridge-port containers
agg-system
key-group
linkagg
bridge
component
bridges
Box 1b YANG Model
[ bridge-port ]
[ lag ]
ieee8023adLag
MACs in LAG are interfaces of type ethernetCsmacd augmented with ethernet, aggport, and inhibit-bridge-port containers
aggport and lag containers include a leaf pointing to the key-group to which theses interfaces are assigned
Linkages between aggport and lag containers are not configured. They are established dynamically by LACP, and readable in the interface higher-layer-if and lower-layer-if lists.
Add linkagg container with a single agg-system and, in this case, a single key-group

## Slide 7: Bridge Notes
These examples use a version of the standard ieee-dot1q-bridge.yang module modified to include edits from:
  Maintenance Item 0370 which introduces the “inhibit-bridge-port” presence container to allow ethernetCsmacd interfaces to prevent automatic augmentation with a “bridge-port” container.
    The proposed solution in Maintenance Item 0370 uses the name “no-bridge-port” for the presence container that inhibits automatic augmentation. Ideally this can be changed to “inhibit-bridge-port” when put into 802.1Q-2022-Rev.
  Maintenance Item 0383 which allows the system to provide the unique MAC address to be used as a bridge identifier, rather than requiring it to be explicitly configured in a YANG model.

## Slide 8: Link Aggregation in other Systems
These models can be adapted to systems that are not bridges (e.g., routers, servers, firewalls, …).
  Replace “bridges” container with container(s) that include per-system configuration and status values for the core functionality of the system.
  Replace “bridge-port” container with container(s) that include port-specific configuration and status values for the functionality of the system.

## Slide 9: Details and Variations

## Slide 10: Link Aggregation variation 1
If MAC-2 and MAC-3 are connected to different systems, only one will attach to the Aggregator (ieee8023adLag interface).
  Which MAC attaches is system implementation dependent.
  The link on the MAC not attached to the Aggregator will be operational but will not pass any frames because it is not attached to a higher layer.
  This may be appropriate …
    If there is specific functionality configured on just this bridge-port, regardless of whether that bridge-port is supported by a LAG or a solitary link, and cannot be supported on an additional bridge-port.
  This may be intentional …
    This configuration supports the “dual-homed” topology, where only one link is active at a time, but the other will become active if the first fails.
    Particularly useful when attached to MC-LAG, DRNI, or other high availability dual-system function, because it can help prevent loops in case of a “split-brain” condition.
Alternatively …
    If the functionality on this bridge-port is generic, and the bridge can support another bridge-port, then can add another ieee8023adLag interface to the key-group which would allow the MACs to either come up as two solitary links, or come up together as a LAG.

## Slide 11: Link Aggregation variation 2
MAC-1 does not run LACP
  Why enable LACP on this MAC?
    Allows it to participate as a passive partner, rather than a silent partner, when connected to another system that would allow the link to be in an aggregation with other links.
  Enabling LACP entails:
    Creating another key-group configured so that any member of this key group is limited to being a solitary link (the aggregation bit of the actor-admin-state is clear).
    Augmenting the MAC-1 interface with an aggport and inhibit-bridge-port containers instead of a bridge-port container.
    Adding an ieee8023adLag interface augmented with lag and bridge-port containers.
  Multiple MACs can reference the same key-group, and each will be a solitary (non-aggregated) link.

## Slide 12: Box 1b variations 1 and 2 “baggy pants” diagram
Agg Port
Agg Port
MAC-1
Box 1b
MAC Relay
MAC-2
MAC-3
()
()
()
()
Aggregator
Agg Port
()
()
Aggregator
Aggregator
Link Aggregation variation 2 to enable MAC-1 to exchange LACPDUs with an active partner
Link Aggregation variation 1 to allow both links to come up if connected to different systems

## Slide 13
key-group-2and3
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-2
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-3
Link Aggregation variation 2
Link Aggregation variation 1:
When MAC-2 and MAC-3 form a LAG, this interface will not be operational (oper-status = down)
When MAC-2 and MAC-3 connect to different systems, one MAC will attach to this Aggregator and this interface will be operational (oper-status = up).
agg-system
linkagg
bridge
component
bridges
Box 1b YANG Model
variations 1 and 2
[ bridge-port ]
[ lag ]
ieee8023adLag
key-group-1
[ bridge-port ]
[ lag ]
ieee8023adLag
[ bridge-port ]
[ lag ]
ieee8023adLag
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-1
Link Aggregation variation 2
Link Aggregation variation 2

## Slide 14: Plug-and-Play Link Aggregation
Allow the configuration to adapt to the cabling, rather than requiring the cabling to conform to the configuration.
  Use when ports are functionally equivalent.
    This is often the case with bridges, and for at least a subset of ports on other devices.
  LACP automatically forms a LAG when two or more ports are connected to the same device (and that device allows aggregation).
  Simplifies configuration.
  Reduces issues with mis-cabling.
All interfaces (that are augmented with “aggport” or “lag” containers) reference the same key-group.
  That key-group has the “aggregation” bit in the “actor-admin-state” set.
    This bit is set by default, so no explicit configuration is required.

## Slide 15
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-2
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-3
agg-system
linkagg
bridge
component
bridges
Box 1b YANG Model
Plug-and-Play variation
[ bridge-port ]
[ lag ]
ieee8023adLag
key-group
[ bridge-port ]
[ lag ]
ieee8023adLag
[ bridge-port ]
[ lag ]
ieee8023adLag
[ inhibit-bridge-port ]
[ aggport ]
[ ethernet ]
ethernetCsmacd
MAC-1
Link Aggregation Plug-and-Play:
All interfaces reference the same key-group (which has “aggregation” bit set)
LACP will automatically form LAGs when two or more ports are connected to the same device.

## Slide 16: Back-up slides

## Slide 17: Non-standard variation 2 – Implicit Aggregators
The standard way to enable LACP on MAC-1 involves adding an ieee8023adLag interface
  because the Link Aggregation standard only specifies attaching an Aggregation Port to higher layers through an intervening Aggregator.
  When this is a solitary link, the Aggregator is basically a pass-through layer.
The YANG models will support a non-standard configuration short-cut:
  Configure a key-group that only allows solitary links.
  Do not introduce any Aggregators as members of this key-group.
  Any MACs using this short-cut to enable LACP are augmented with both aggport and bridge-port containers.
    The aggport container references the key-group that only allows solitary links.
Caveat:
  The system must recognize this configuration and implement non-standard modifications to LACP that allow a solitary Aggregation Port to attach to higher-layer functionality without an intervening Aggregator.
Risks!
  The YANG model will not prevent an aggport in this configuration from referencing a key-group that allows aggregation. If this happens there is a possibility this port will end up in a LAG with one or more other ports. This would create two paths between the MAC and the MAC Relay, through two different bridge-ports, that are both operational at the same time. Since this is a non-standard implementation, the resulting behavior is unspecified and system-dependent, but unlikely to be desirable and likely to be very disruptive to the network!

## Slide 18: Thank You